## Slide 1
LIFT
CONTROL SYSTEM
SECR1013-03 DIGITAL LOGIC
GROUP 4

## Slide 2
PREPARED BY
Terence Lim Jian Yuan
Wong Jing Jie
James Sim Chia Tai
Ng Yaw Kuan

## Slide 3
OBJECTIVE
  Design a 3-bit synchronous counter for the lift system controller
  Implement basic principles of combinational and sequential logic
  Test and check the functionality of designed circuit using Deeds
  Utilise the components of combinational and sequential circuits
  Develop problem-solving, logical thinking and teamworking skills
  Demonstrate and explain the operation of the lift system

## Slide 4
BACKGROUND
  To implement a 8-level lift system
  Utilise 3-bit synchronous counter
  Added extra authentication features
  Circuits:
- Combinational circuit
- Sequential circuit
- Additional features

## Slide 5
PROBLEM STATEMENT
  Lack strong security systems
  Unauthorised lift access
  Need for authentication from authorised personnel

## Slide 6
  Card + 4-bit Password Protection
  Integrates advanced electronic components:
- 3-bit floor comparator
- 4-bit password comparator
- JK flip-flops as counters
- Basic gates to route signals
SUGGESTED SOLUTION

## Slide 7
BLOCK DIAGRAM

## Slide 8
STATE DIAGRAM

## Slide 9
IMPLEMENTATION

## Slide 10
MAIN FUNCTION (JK FLIP-FLOPS)
  3 JK flip-flops
  Synchronous saturated
up/down counter
  Common clock
  Stop when clock disabler is LOW

## Slide 11
FLOOR SWITCHES
  Uses 8 floor switches
  Encoded into 3-bit destination floor
  Supports multiple selections
  Priority based on the direction of the lift

## Slide 12
CLOCK DISABLER
  5-input AND gate
  HIGH when 5 inputs are HIGH
  Inputs:
- Clock Generator
- Password Comparator
- Floor Comparator
- Card reader
- Power switch
  Start and stop the lift operation

## Slide 13
PASSWORD COMPARATOR
  4-bit MSI Comparator Chip
  Verifies the password entered
  Only outputs HIGH when the password entered is exactly equals to the preset password: “1101”

## Slide 14
FLOOR COMPARATOR
  Uses XNOR + NAND gates
  Compares current floor and desired floor
  Output:
- HIGH → Floors not equal
- LOW → Floors are equal

## Slide 15
SOUND NOTIFICATION
  Configured a JK flip-flop to D flip-flop
  Stores the comparator result one clock cycle earlier
  2-input AND gate
  Operation:
- Floor ≠ Desired: AND=0 →sound OFF
- Floor = Desired: AND= 1 →sound ON
- Next clock: AND=0 →sound OFF

## Slide 16
CURRENT FLOOR DISPLAY
  Shows current floor
  Display in both binary and hex form
  Driven by JK flip-flops

## Slide 17
FULL DIGITAL ELECTRONIC DEEDS CIRCUIT

## Slide 18
CONCLUSION
  Demonstrated the design and implementation of an elevator.
  Designed by implementing a 3-bit synchronous counter and other components.
  These collaboration of components enable the function of the system.

## Slide 19
REFLECTION
  This project enhanced our knowledge in Digital Logic.
  Provided many practical experience in the application of digital electronics concepts.
  We’re excited to implement more complex circuit in the future.

## Slide 20
THANK YOU